## Slide 1: Power Plant Overview & More
Miami Fort Station
October 2022
Sean Behm, Environmental & Chemistry Manager

## Slide 2: Discussion Topics
Power Plant Operation
  How Electricity is Made
  How Steam is Made
  Environmental Controls
  Byproducts
Electrical Grid Overview
  Robustness & Fragility – Columbus June 2022 event
Energy & Electricity Trends (EIA)

## Slide 3: ELECTRICITY - WATT IS IT?
The movement of electrons through a conductor
Measured in Watts= Voltage X Current
Made & Used INSTANTANEOUSLY
Miami Fort Station
Produces 1,100 Mega Watts
Or
1,100,000,000 Watts
Or
Enough electricity to light 11,000,000 100-watt lights bulbs at once…even more LEDs!
Enough electricity to power nearly 800,000 homes

## Slide 4: ELECTRICTY - How is it made?
Generator Facts
Similar to a large electric motor
The turbine shaft is connected to the shaft of the generator, where magnets spin within wire coils to produce electricity
Rotor spins at 3600RPMs = 60Hz
  60 revolutions per second
Generator produces 22,000 volts of electricity at 18,000 amps
Cooled with Hydrogen Gas

## Slide 5: How do coal fired power plants work?

## Slide 6: ELECTRICITY - How does it get to your house?
Electric Transmission Facts
From the generating stations, large amounts of electricity are transported on transmission lines.
Next, substations convert the transmission line voltage to lower levels that are used in local communities. Substations also control the flow of electricity and protect the lines and equipment from damage.
A transformer converts the distribution level voltage to levels that can be used inside your home or business. That voltage ranges from 120 to 480 volts.

## Slide 7: ELECTRICITY – Miami Fort Switchyard Picture

## Slide 8: Component- COAL
Miami Fort Station Facts
Receives all its coal on river barges.
Coal comes from OH, KY, WV, IL.
Burns approximately 12,500 tons per day or 4.0 million tons per year
All coal is different

## Slide 9: Coal Barge Unloader – Additional Pictures

## Slide 10: Component- Bunker and Feeder Pictures

## Slide 11: Component- Pulverizer Pictures

## Slide 12: Component- Boiler
Boilers can produce flame temps of greater than 3,000°F at with steam pressures greater than 2,700 psi
1005°F superheated steam is then piped to the turbine

## Slide 13: Component- Boiler Pictures
W. H. Zimmer Power Plant Steam Generator, largest formerly operating boiler in the world

## Slide 14: Component- Boiler Pictures

## Slide 15: Component- Boiler problems
Boiler Tube Failures - #1 Cause of Forced Outages at plant
Poor Combustion / Overheating / Slag
Corrosion / Erosion
  Coal Specs
OUTAGES!!!! LOST $$$$

## Slide 16: Component- Steam Turbines
G
Mechanical device that extracts thermal energy from pressurized steam and converts it into useful mechanical work.
  Rotates at 3,600 RPM’s
The high pressure steam (2,400 psi @ 1,005°F) drives the turbine through a series of “blades” which rotates the turbine shaft.
  The turbine shaft is connected to the shaft of the generator.
  The exhausted steam is condensed and returned to the boiler to go through the process again.

## Slide 17: Component- Steam Turbine – Unit 7 Turbine

## Slide 18: Component- Steam Turbines – Unit 8 Turbine Deck
Unit 6
Unit 5
Unit 4
Unit 3
Unit 8

## Slide 19: Component- Cooling Tower
Water Vapor
Heat
Natural Draft Cooling Tower
The circulating cooling water is cycled between these types of towers and the condenser. The heat in the falling water is carried away by the upward air draft in the towers.

## Slide 20: Control Room

## Slide 21: Component- Environmental Control
Selective Catalytic Reduction- SCR’s.
  Removes reduces 92% Nitrogen Oxide (NOx) emissions.
  Similar to catalytic converter in a car - ammonia is oxidized, NOx is reduced.
Electrostatic Precipitators- ESP’s.
  Removes approximately 99.9% Fly Ash from the flue gas stream.
  Fly ash is usable product.
Flue Gas De-Sulfurization- FGD.
  Removes 97% Sulfur Dioxide (SO2) emissions.
  SO2 can cause “acid rain”.
  Sulfur is naturally contained in the coal.
  Uses lime or limestone (CaCO3) to remove (scrub) the SO2 from the flue gas.
  Usable by-product is Gypsum for wall board manufacturing.
peregrine falcon

## Slide 22: Component- Environmental Control
NOx
SO2
Solid Particles
SO2
Solid Particles
NOx
Flue Gases

## Slide 23: Component- Byproducts
Bottom Ash
  Used in structural fills for ODOT.
  Sandblasting media.
  Miami Fort will produce ~70,000 tons per year.
Fly Ash
  Used in concrete pavers.
  Filler for cement.
  Miami Fort will produce ~ 390,000 tons per year.
Gypsum
  The FGD Process creates a byproduct called Gypsum.
  Gypsum is used to make drywall.
  Miami Fort will produce ~2,000 tons per day.
    Enough gypsum to make: 95 semi-truck loads of drywall every day or build ~75,000 homes per year.

## Slide 24: What is important to us?
Safety
The safety of our employees, contractors, and guest
Everyone goes home safe to their family every day
Reliability
Providing an essential service to the public
Making Power is how we make money as a business
Environment
We care about our community and protecting the air we all breath and the water we drink
Environmental Compliance is critical to our success

## Slide 25: Miami Fort Power Station- Over 95 Years of Operation
1926
2021

## Slide 26: Market Information
PJM (Pennsylvania, New Jersey, and Maryland)
  As the primary task, to ensure the safety, reliability and security of the bulk electric power system.
  Create and operate robust, competitive and non-discriminatory electric power markets.
  Understand customer needs and deliver valued service to meet those needs in a cost-efficient manner.
https://www.luminant.com/about/

## Slide 27: Electric Grid & Generation – Cincinnati - 345 kV
Source: atlas.eia.gov

## Slide 28: Electric Grid & Generation – Cincinnati – 69 kV+
Source: atlas.eia.gov

## Slide 29: Electric Grid & Generation – Columbus – 69 kV+
Source: atlas.eia.gov

## Slide 30: June 13-16th Event – PJM - AEP Load Zone - Columbus
Source: emergencyprocedures.pjm.com

## Slide 31: News Articles regarding Columbus June Outages

## Slide 32
https://www.pjm.com/-/media/markets-ops/demand-response/estimated-demand-response-june-14-15-16-2022.ashx

## Slide 33
www.pjm.com/-/media/committees-groups/committees/oc/2022/20220714/item-03---june-14-16-operations-review.ashx

## Slide 34: Energy Trends
Sourced from EIA (Energy Information Administration) – 2022 Annual Energy Outlook

## Slide 35: Energy production and consumption
Chart: 
Chart: 
Energy production by source
AEO2022 Reference case
quadrillion British thermal units
Energy consumption by fuel
AEO2022 Reference case
quadrillion British thermal units
Note: Biofuels are shown separately and included in petroleum and other liquids.

## Slide 36: U.S. natural gas production and prices
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Low Oil and Gas Supply | 19.182 | 19.6163 | 18.9278 | 19.0985 | 18.5909 | 18.0506 | 18.5036 | 19.266 | 20.1586 | 20.6239 | 21.3155 | 22.9019 | 24.0333 | 24.2055 | 25.8896 | 27.0655 | 26.5921 | 27.3063 | 30.7743 | 33.899 | 33.4853 | 34.4042 | 35.1003 | 34.2033 | 33.4217 | 32.7093 | 31.9985 | 31.5957 | 31.3035 | 31.1212 | 30.6143 | 30.3854 | 30.2793 | 30.0439 | 29.8365 | 29.7591 | 29.8028 | 29.6504 | 29.5685 | 29.4776 | 29.343 | 29.198 | 29.0904 | 28.8948 | 29.1328 | 28.8788 | 28.7443 | 28.6667 | 28.6864 | 28.5989 | 28.6326
High Oil and Gas Supply | 19.182 | 19.6163 | 18.9278 | 19.0985 | 18.5909 | 18.0506 | 18.5036 | 19.266 | 20.1586 | 20.6239 | 21.3155 | 22.9019 | 24.0333 | 24.2055 | 25.8896 | 27.0655 | 26.5921 | 27.3063 | 30.7743 | 33.899 | 33.4853 | 34.4089 | 35.8733 | 36.9703 | 38.1635 | 38.9174 | 39.2872 | 39.8333 | 41.0739 | 41.6891 | 42.2484 | 42.7472 | 43.3323 | 44.589 | 45.0933 | 45.4279 | 45.7921 | 46.2719 | 46.8029 | 47.3926 | 48.1697 | 48.7078 | 49.1127 | 49.6134 | 50.0928 | 50.424 | 50.9806 | 51.481 | 52.026 | 52.3806 | 52.8849
Reference | 19.182 | 19.6163 | 18.9278 | 19.0985 | 18.5909 | 18.0506 | 18.5036 | 19.266 | 20.1586 | 20.6239 | 21.3155 | 22.9019 | 24.0333 | 24.2055 | 25.8896 | 27.0655 | 26.5921 | 27.3063 | 30.7743 | 33.899 | 33.4853 | 34.4042 | 35.6859 | 36.0523 | 36.4096 | 36.4846 | 36.5705 | 36.7197 | 37.2603 | 37.5132 | 37.622 | 37.9323 | 38.3465 | 38.5041 | 38.5987 | 38.5955 | 38.705 | 38.8937 | 39.1462 | 39.3503 | 39.641 | 39.9667 | 40.2675 | 40.5177 | 41.0303 | 41.325 | 41.571 | 41.82 | 42.0588 | 42.2596 | 42.5823
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Low Oil and Gas Supply | 6.2565 | 5.6251 | 4.7264 | 7.5096 | 7.8741 | 11.2664 | 8.4691 | 8.5416 | 10.6505 | 4.7004 | 5.1533 | 4.6205 | 3.1168 | 4.1546 | 4.7791 | 2.8382 | 2.7016 | 3.1463 | 3.2369 | 2.5845 | 2.0249 | 4.107 | 4.4739 | 4.3643 | 4.2413 | 4.2277 | 4.3386 | 4.4306 | 4.7093 | 4.9813 | 5.155 | 5.355 | 5.5384 | 5.7004 | 5.8131 | 5.8766 | 6.0666 | 6.1215 | 6.1915 | 6.3119 | 6.4379 | 6.4017 | 6.3335 | 6.284 | 6.4222 | 6.4613 | 6.5179 | 6.5577 | 6.5968 | 6.6744 | 6.74
High Oil and Gas Supply | 6.2565 | 5.6251 | 4.7264 | 7.5096 | 7.8741 | 11.2664 | 8.4691 | 8.5416 | 10.6505 | 4.7004 | 5.1533 | 4.6205 | 3.1168 | 4.1546 | 4.7791 | 2.8382 | 2.7016 | 3.1463 | 3.2369 | 2.5845 | 2.0249 | 4.1079 | 3.555 | 3.0637 | 2.6523 | 2.4581 | 2.3963 | 2.4326 | 2.5702 | 2.6457 | 2.7203 | 2.7484 | 2.7582 | 2.8355 | 2.8329 | 2.7982 | 2.7838 | 2.7787 | 2.7552 | 2.7645 | 2.74 | 2.7012 | 2.6391 | 2.6164 | 2.5964 | 2.5836 | 2.565 | 2.5245 | 2.5297 | 2.5322 | 2.5404
Low Oil Price Case | 6.2565 | 5.6251 | 4.7264 | 7.5096 | 7.8741 | 11.2664 | 8.4691 | 8.5416 | 10.6505 | 4.7004 | 5.1533 | 4.6205 | 3.1168 | 4.1546 | 4.7791 | 2.8382 | 2.7016 | 3.1463 | 3.2369 | 2.5845 | 2.0249 | 4.1077 | 3.6178 | 3.4702 | 3.4725 | 3.3395 | 3.24 | 3.274 | 3.3783 | 3.4155 | 3.3952 | 3.4407 | 3.4784 | 3.5184 | 3.5665 | 3.5916 | 3.6382 | 3.6357 | 3.6217 | 3.5786 | 3.5488 | 3.5385 | 3.5189 | 3.5128 | 3.5432 | 3.5464 | 3.524 | 3.5214 | 3.5205 | 3.5188 | 3.5411
High Oil Price Case | 6.2565 | 5.6251 | 4.7264 | 7.5096 | 7.8741 | 11.2664 | 8.4691 | 8.5416 | 10.6505 | 4.7004 | 5.1533 | 4.6205 | 3.1168 | 4.1546 | 4.7791 | 2.8382 | 2.7016 | 3.1463 | 3.2369 | 2.5845 | 2.0249 | 4.1077 | 3.8358 | 3.2352 | 2.8915 | 2.8054 | 2.7596 | 2.8445 | 3.0149 | 3.1917 | 3.3215 | 3.4462 | 3.5676 | 3.6405 | 3.6223 | 3.5719 | 3.5421 | 3.5824 | 3.6434 | 3.6734 | 3.7764 | 3.8219 | 3.7687 | 3.7411 | 3.7426 | 3.7064 | 3.677 | 3.6904 | 3.6698 | 3.7136 | 3.7409
Reference | 6.2565 | 5.6251 | 4.7264 | 7.5096 | 7.8741 | 11.2664 | 8.4691 | 8.5416 | 10.6505 | 4.7004 | 5.1533 | 4.6205 | 3.1168 | 4.1546 | 4.7791 | 2.8382 | 2.7016 | 3.1463 | 3.2369 | 2.5845 | 2.0249 | 4.1077 | 3.8432 | 3.4932 | 3.1748 | 3.0008 | 2.9781 | 3.0755 | 3.2468 | 3.3647 | 3.4597 | 3.5438 | 3.5774 | 3.6458 | 3.6401 | 3.6379 | 3.6478 | 3.665 | 3.6839 | 3.685 | 3.7205 | 3.7266 | 3.7038 | 3.7074 | 3.6451 | 3.6145 | 3.6031 | 3.5969 | 3.6211 | 3.5976 | 3.5904
Natural gas spot price at Henry Hub
AEO2022 side cases
2021 dollars per million British thermal unit
U.S. dry natural gas production
AEO2022 oil and gas supply cases
trillion cubic feet
2021
history projections
High Oil and
Gas Supply
Reference
Low Oil and
Gas Supply

## Slide 37: U.S. dry natural gas production
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
"other" | 1.9115 | 2.0059 | 2.0914 | 2.224 | 2.2107 | 2.2798 | 2.2789 | 2.2988 | 2.3738 | 2.3703 | 2.2508 | 2.1174 | 1.998 | 1.7844 | 1.6631 | 1.547 | 1.4104 | 1.3232 | 1.277 | 1.2001 | 1.088 | 1.1542 | 1.0927 | 1.0563 | 1.0612 | 1.0757 | 1.0874 | 1.0885 | 1.0875 | 1.0745 | 1.0664 | 1.0527 | 1.0429 | 1.0236 | 1.0055 | 0.99975 | 0.9896 | 0.95897 | 0.94641 | 0.9078 | 0.87417 | 0.86931 | 0.85622 | 0.82896 | 0.81483 | 0.80641 | 0.8066 | 0.79583 | 0.79692 | 0.78954 | 0.75787
Lower 48 offshore | 5.261 | 5.5194 | 4.9942 | 4.8773 | 4.3712 | 3.4696 | 3.2321 | 3.1202 | 2.6522 | 2.7149 | 2.4992 | 2.0468 | 1.6189 | 1.413 | 1.3485 | 1.3585 | 1.25 | 1.0798 | 0.9754 | 1.0152 | 0.76364 | 1.0182 | 0.75009 | 0.73429 | 0.77839 | 0.81237 | 0.85102 | 0.87485 | 1.017 | 1.0374 | 1.1257 | 1.2309 | 1.2045 | 1.3366 | 1.3648 | 1.356 | 1.3304 | 1.2639 | 1.304 | 1.317 | 1.3281 | 1.2491 | 1.2969 | 1.2599 | 1.3362 | 1.4237 | 1.4367 | 1.4046 | 1.3421 | 1.4651 | 1.5574
other Lower 48 onshore | 5.8745 | 5.7924 | 5.4677 | 5.3878 | 5.2025 | 5.048 | 5.0239 | 4.8645 | 4.7926 | 4.4585 | 4.1536 | 3.9059 | 3.6478 | 3.4522 | 3.4061 | 3.1685 | 2.7819 | 2.6426 | 2.578 | 2.4206 | 2.2505 | 2.3247 | 2.0977 | 1.9778 | 1.8936 | 1.8378 | 1.6988 | 1.5973 | 1.5231 | 1.4712 | 1.432 | 1.3833 | 1.3452 | 1.302 | 1.2636 | 1.2367 | 1.2128 | 1.2026 | 1.1979 | 1.1931 | 1.2077 | 1.2114 | 1.1866 | 1.1764 | 1.1557 | 1.1344 | 1.1147 | 1.099 | 1.0803 | 1.0629 | 1.0543
tight/shale gas | 6.1351 | 6.2986 | 6.3744 | 6.6094 | 6.8065 | 7.2531 | 7.9686 | 8.9826 | 10.34 | 11.0801 | 12.4119 | 14.8318 | 16.7638 | 17.556 | 19.4733 | 20.9553 | 21.1512 | 22.2824 | 25.9314 | 29.258 | 29.5702 | 29.9071 | 31.7455 | 32.2839 | 32.6764 | 32.7587 | 32.9333 | 33.1591 | 33.6327 | 33.9302 | 33.9979 | 34.2655 | 34.7539 | 34.8419 | 34.9648 | 35.003 | 35.1722 | 35.4682 | 35.6979 | 35.9323 | 36.231 | 36.6368 | 36.9278 | 37.2525 | 37.7236 | 37.9605 | 38.213 | 38.5206 | 38.8395 | 38.9421 | 39.2126
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
"other" | 1.9115 | 2.0059 | 2.0914 | 2.224 | 2.2107 | 2.2798 | 2.2789 | 2.2988 | 2.3738 | 2.3703 | 2.2508 | 2.1174 | 1.998 | 1.7844 | 1.6631 | 1.547 | 1.4104 | 1.3232 | 1.277 | 1.2001 | 1.088 | 1.1312 | 1.0214 | 0.98628 | 1.0117 | 1.0425 | 1.0499 | 1.0561 | 1.051 | 1.0471 | 1.0397 | 1.0187 | 1.013 | 0.99702 | 0.97961 | 0.96005 | 0.94468 | 0.92549 | 0.89917 | 0.88505 | 0.8679 | 0.85255 | 0.83704 | 0.82444 | 0.81306 | 0.81032 | 0.77935 | 0.77703 | 0.76733 | 0.77155 | 0.76721
Lower 48 offshore | 5.261 | 5.5194 | 4.9942 | 4.8773 | 4.3712 | 3.4696 | 3.2321 | 3.1202 | 2.6522 | 2.7149 | 2.4992 | 2.0468 | 1.6189 | 1.413 | 1.3485 | 1.3585 | 1.25 | 1.0798 | 0.9754 | 1.0152 | 0.76363 | 1.0172 | 0.73546 | 0.74301 | 0.793 | 0.88066 | 0.94922 | 1.002 | 1.1822 | 1.2333 | 1.2638 | 1.369 | 1.46 | 1.578 | 1.6482 | 1.7988 | 1.8981 | 1.979 | 1.9383 | 1.9231 | 2.0955 | 2.1863 | 2.3083 | 2.3458 | 2.4655 | 2.5928 | 2.6506 | 2.9254 | 2.8391 | 2.5748 | 2.4275
other Lower 48 onshore | 5.8745 | 5.7924 | 5.4677 | 5.3878 | 5.2025 | 5.048 | 5.0239 | 4.8645 | 4.7926 | 4.4585 | 4.1536 | 3.9059 | 3.6478 | 3.4522 | 3.4061 | 3.1685 | 2.7819 | 2.6426 | 2.578 | 2.4206 | 2.2505 | 2.3337 | 2.038 | 1.9196 | 1.8452 | 1.8111 | 1.6829 | 1.5941 | 1.5241 | 1.4721 | 1.4331 | 1.3833 | 1.343 | 1.2983 | 1.2593 | 1.2241 | 1.1973 | 1.1857 | 1.1808 | 1.1815 | 1.1908 | 1.1931 | 1.1657 | 1.1532 | 1.1338 | 1.1123 | 1.0914 | 1.0739 | 1.0561 | 1.0372 | 1.0273
tight/shale gas | 6.1351 | 6.2986 | 6.3744 | 6.6094 | 6.8065 | 7.2531 | 7.9686 | 8.9826 | 10.34 | 11.0801 | 12.4119 | 14.8318 | 16.7638 | 17.556 | 19.4733 | 20.9553 | 21.1512 | 22.2824 | 25.9314 | 29.258 | 29.5699 | 29.9267 | 32.0785 | 33.3215 | 34.5136 | 35.183 | 35.6051 | 36.1812 | 37.3166 | 37.9366 | 38.5118 | 38.9762 | 39.5163 | 40.7157 | 41.2061 | 41.445 | 41.752 | 42.1818 | 42.7847 | 43.4028 | 44.0156 | 44.4758 | 44.8016 | 45.2899 | 45.6805 | 45.9086 | 46.4593 | 46.7047 | 47.3635 | 47.997 | 48.6629
Chart: 
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
"other" | 1.9115 | 2.0059 | 2.0914 | 2.224 | 2.2107 | 2.2798 | 2.2789 | 2.2988 | 2.3738 | 2.3703 | 2.2508 | 2.1174 | 1.998 | 1.7844 | 1.6631 | 1.547 | 1.4104 | 1.3232 | 1.277 | 1.2001 | 1.088 | 1.1483 | 1.1206 | 1.1357 | 1.1616 | 1.1848 | 1.188 | 1.1879 | 1.1772 | 1.1616 | 1.1449 | 1.1427 | 1.1308 | 1.0739 | 1.0674 | 1.066 | 1.0564 | 1.0113 | 0.96626 | 0.9394 | 0.92122 | 0.9121 | 0.857 | 0.82922 | 0.82198 | 0.79914 | 0.78667 | 0.77972 | 0.76355 | 0.71942 | 0.67332
Lower 48 offshore | 5.261 | 5.5194 | 4.9942 | 4.8773 | 4.3712 | 3.4696 | 3.2321 | 3.1202 | 2.6522 | 2.7149 | 2.4992 | 2.0468 | 1.6189 | 1.413 | 1.3485 | 1.3585 | 1.25 | 1.0798 | 0.9754 | 1.0152 | 0.76363 | 1.0185 | 0.75865 | 0.72278 | 0.62828 | 0.59466 | 0.60986 | 0.59354 | 0.64068 | 0.65538 | 0.706 | 0.71132 | 0.6757 | 0.72213 | 0.78484 | 0.89241 | 0.86547 | 0.84846 | 0.87416 | 0.83559 | 0.78386 | 0.91407 | 1.0651 | 1.0543 | 1.0462 | 0.87509 | 0.80853 | 0.75473 | 0.8756 | 0.85354 | 0.93024
other Lower 48 onshore | 5.8745 | 5.7924 | 5.4677 | 5.3878 | 5.2025 | 5.048 | 5.0239 | 4.8645 | 4.7926 | 4.4585 | 4.1536 | 3.9059 | 3.6478 | 3.4522 | 3.4061 | 3.1685 | 2.7819 | 2.6426 | 2.578 | 2.4206 | 2.2505 | 2.326 | 2.1396 | 2.0298 | 1.941 | 1.8748 | 1.7197 | 1.6075 | 1.5328 | 1.4784 | 1.4368 | 1.3922 | 1.3568 | 1.3118 | 1.2757 | 1.2433 | 1.2188 | 1.2091 | 1.2064 | 1.2089 | 1.2246 | 1.2209 | 1.1846 | 1.1657 | 1.1509 | 1.1293 | 1.1115 | 1.0964 | 1.0778 | 1.0635 | 1.0527
tight/shale gas | 6.1351 | 6.2986 | 6.3744 | 6.6094 | 6.8065 | 7.2531 | 7.9686 | 8.9826 | 10.34 | 11.0801 | 12.4119 | 14.8318 | 16.7638 | 17.556 | 19.4733 | 20.9553 | 21.1512 | 22.2824 | 25.9314 | 29.258 | 29.57 | 29.9115 | 31.0815 | 30.315 | 29.6908 | 29.055 | 28.4809 | 28.2068 | 27.9529 | 27.8258 | 27.3266 | 27.1392 | 27.116 | 26.9361 | 26.7086 | 26.5574 | 26.6621 | 26.5816 | 26.5217 | 26.4936 | 26.4133 | 26.151 | 25.9836 | 25.8456 | 26.1137 | 26.0753 | 26.0376 | 26.0358 | 25.9695 | 25.9625 | 25.9763
Low Oil and Gas Supply case
trillion cubic feet
High Oil and Gas Supply case
trillion cubic feet
Reference case
trillion cubic feet
tight &
shale gas
other Lower
48 states
onshore
Lower 48
states
offshore
other
Dry natural gas production, AEO2022 oil and natural gas supply cases
Note: Tight and shale gas includes tight gas, shale gas, and natural gas from tight oil formations.

## Slide 38: U.S. electricity generation and shares from selected fuels and renewable sources
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
coal | 1847.2903 | 1733.43 | 1514.0429 | 1581.1147 | 1581.7103 | 1352.3982 | 1239.1487 | 1205.8353 | 1149.4873 | 964.9568 | 773.8053 | 954.0652 | 910.0402 | 889.2256 | 759.2833 | 738.0865 | 729.9785 | 724.8306 | 717.0047 | 695.2988 | 684.3961 | 675.6702 | 661.8643 | 668.4832 | 631.0241 | 612.9448 | 590.3401 | 579.7266 | 577.52 | 575.0085 | 564.3532 | 559.2745 | 553.7539 | 545.9753 | 537.7507 | 531.2852 | 528.7425 | 524.9899 | 523.2586 | 522.9271 | 523.6989
nuclear | 806.9683 | 790.2044 | 769.3312 | 789.0165 | 797.166 | 797.1779 | 805.6939 | 804.9496 | 807.0845 | 809.4093 | 789.9186 | 777.6822 | 783.6156 | 785.4799 | 788.9731 | 781.7759 | 773.3351 | 759.4032 | 721.8088 | 715.1594 | 707.0017 | 708.095 | 708.8534 | 668.1328 | 668.8273 | 670.2323 | 671.2769 | 665.0948 | 665.3054 | 664.8966 | 665.356 | 666.5413 | 667.8084 | 668.6749 | 669.4373 | 670.2554 | 670.6824 | 671.1079 | 661.6078 | 661.929 | 662.3925
renewables | 429.7867 | 517.1614 | 500.7242 | 530.205 | 549.812 | 558.3803 | 628.2575 | 710.573 | 736.3551 | 763.6302 | 834.236 | 878.7914 | 974.6796 | 1061.8519 | 1201.2429 | 1298.8636 | 1347.5015 | 1378.3197 | 1425.3744 | 1499.5752 | 1562.8848 | 1600.3682 | 1634.2194 | 1687.256 | 1753.9919 | 1818.7246 | 1874.4916 | 1916.4445 | 1946.1279 | 1980.4126 | 2012.05 | 2037.6404 | 2070.4326 | 2113.1404 | 2139.9006 | 2176.4312 | 2215.0432 | 2254.6433 | 2297.0686 | 2340.4045 | 2384.6184
natural gas | 987.6972 | 1013.6889 | 1225.8942 | 1124.8356 | 1126.609 | 1333.4821 | 1378.3069 | 1296.4425 | 1469.1327 | 1585.8142 | 1616.748 | 1564.1349 | 1539.557 | 1570.1195 | 1587.4219 | 1554.3707 | 1550.9579 | 1561.1512 | 1582.0199 | 1563.2073 | 1541.635 | 1541.7028 | 1550.7772 | 1562.2382 | 1563.9312 | 1554.2781 | 1562.4941 | 1583.4559 | 1603.2281 | 1617.2731 | 1638.6067 | 1666.3652 | 1689.4192 | 1706.2039 | 1739.0846 | 1763.2244 | 1780.978 | 1799.0813 | 1820.2979 | 1835.5157 | 1855.9246
petroleum & other | 55.728 | 49.4815 | 43.9237 | 48.9239 | 49.5414 | 50.3018 | 44.0803 | 40.4605 | 45.757 | 39.0023 | 36.117 | 27.8928 | 27.4882 | 28.0694 | 27.2836 | 27.0689 | 26.511 | 25.8391 | 25.239 | 24.8607 | 24.3693 | 23.7163 | 23.2946 | 23.1087 | 22.9462 | 22.8501 | 22.4762 | 22.5082 | 22.3011 | 22.1063 | 21.8925 | 21.4052 | 20.937 | 20.1765 | 19.6095 | 19.1259 | 18.9276 | 18.3841 | 18.3808 | 17.7756 | 17.5171
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
other | 56.0894 | 56.6708 | 57.6222 | 60.858 | 63.9894 | 63.6319 | 62.7605 | 62.7334 | 61.8319 | 57.507 | 56.0545 | 61.2591 | 61.0936 | 62.9335 | 64.0935 | 65.6668 | 66.7862 | 67.8553 | 68.3589 | 69.6594 | 70.6333 | 72.1263 | 73.6472 | 75.095 | 76.1128 | 77.4193 | 78.6607 | 79.9728 | 81.6224 | 82.552 | 83.6186 | 84.8839 | 86.0924 | 87.5451 | 88.8014 | 89.6758 | 90.6093 | 91.8071 | 92.5129 | 93.7809 | 94.799
hydroelectric | 260.2031 | 319.3549 | 276.2402 | 268.5654 | 259.3666 | 249.0801 | 267.8122 | 300.3329 | 292.524 | 287.8737 | 291.1108 | 259.7296 | 271.3385 | 286.7379 | 300.6847 | 300.9504 | 300.869 | 300.8654 | 300.6857 | 300.7665 | 300.1929 | 299.4545 | 299.3445 | 299.0614 | 298.7615 | 298.8623 | 298.4616 | 298.3417 | 297.8172 | 296.8436 | 297.2078 | 297.7209 | 296.6051 | 295.3538 | 295.6725 | 295.7352 | 295.5706 | 295.187 | 291.1796 | 289.4344 | 289.4466
geothermal | 15.2192 | 15.3161 | 15.5624 | 15.7747 | 15.8769 | 15.9176 | 15.8258 | 15.9268 | 15.9671 | 15.4727 | 16.9301 | 15.86 | 15.8673 | 15.8962 | 15.879 | 16.9889 | 18.0729 | 19.3572 | 20.6874 | 22.1828 | 23.5455 | 24.7543 | 26.4886 | 27.9706 | 29.7477 | 31.4795 | 33.1974 | 34.8064 | 36.2715 | 37.6168 | 39.0323 | 40.3086 | 41.1785 | 42.0682 | 43.2901 | 44.4654 | 45.3463 | 45.8853 | 46.3696 | 46.883 | 47.38
wind | 94.6522 | 120.1766 | 140.8217 | 167.8397 | 181.6553 | 190.7185 | 226.9926 | 254.3027 | 272.6675 | 295.8825 | 337.5098 | 377.6656 | 422.3198 | 439.5988 | 464.2495 | 519.0156 | 541.3367 | 547.8514 | 556.3535 | 566.9195 | 593.5239 | 600.5453 | 602.2605 | 603.9323 | 621.0452 | 648.707 | 661.3048 | 669.7364 | 672.265 | 673.7101 | 677.934 | 682.1479 | 689.5551 | 700.8303 | 700.5721 | 704.1688 | 713.7246 | 719.2849 | 722.0703 | 727.196 | 737.0348
solar | 3.6228 | 5.643 | 10.4777 | 17.1672 | 28.9237 | 39.0322 | 54.8665 | 77.2771 | 93.3646 | 106.8943 | 132.6308 | 164.277 | 204.0604 | 256.6856 | 356.3361 | 396.2419 | 420.4366 | 442.3903 | 479.2888 | 540.0472 | 574.9891 | 603.4877 | 632.4786 | 681.1967 | 728.3248 | 762.2565 | 802.8669 | 833.587 | 858.1519 | 889.6899 | 914.2574 | 932.579 | 957.0016 | 987.343 | 1011.5642 | 1042.386 | 1069.7925 | 1102.479 | 1144.9359 | 1183.11 | 1215.9583

## Slide 39: U.S. electricity generation levels from selected fuels and renewable sources
Chart: 
Note: Renewables category includes electricity generation from wind, solar, hydroelectric, geothermal, wood, and other biomass sources.
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
coal | 1847.2903 | 1733.43 | 1514.0429 | 1581.1147 | 1581.7103 | 1352.3982 | 1239.1487 | 1205.8353 | 1149.4873 | 964.9568 | 773.8053 | 954.0651 | 918.9001 | 880.147 | 756.0094 | 730.4811 | 715.2285 | 703.3857 | 674.0838 | 659.1894 | 642.4052 | 623.4288 | 600.6688 | 609.732 | 577.231 | 544.3731 | 522.7756 | 491.0301 | 487.2462 | 478.6077 | 454.7193 | 440.0386 | 427.9645 | 420.3622 | 412.0604 | 385.7827 | 371.8839 | 360.9655 | 351.8619 | 344.7248 | 326.8783
renewables | 427.3761 | 513.3361 | 494.5732 | 522.0734 | 538.5793 | 544.241 | 609.4451 | 686.5827 | 706.8158 | 728.6727 | 792.4961 | 878.795 | 973.813 | 1060.0316 | 1199.9419 | 1302.2726 | 1370.8833 | 1452.4507 | 1507.6379 | 1575.6573 | 1670.8715 | 1764.3307 | 1841.4334 | 1900.3174 | 1983.4473 | 2111.9465 | 2213.1289 | 2276.1597 | 2325.5439 | 2371.2222 | 2446.6355 | 2531.187 | 2600.6738 | 2660.4031 | 2753.8423 | 2828.5015 | 2905.2717 | 3008.3208 | 3086.8008 | 3156.1785 | 3240.4373
natural gas | 987.6972 | 1013.6889 | 1225.8942 | 1124.8356 | 1126.609 | 1333.4821 | 1378.3069 | 1296.4425 | 1469.1327 | 1585.8142 | 1616.748 | 1564.2129 | 1524.8704 | 1576.4982 | 1587.5879 | 1555.0446 | 1540.0747 | 1507.4946 | 1573.7853 | 1548.6217 | 1500.6349 | 1454.6307 | 1437.7834 | 1461.7985 | 1477.6803 | 1440.7775 | 1412.6456 | 1435.199 | 1454.0143 | 1473.061 | 1464.349 | 1490.2155 | 1486.6055 | 1489.7275 | 1495.7302 | 1524.5823 | 1537.8042 | 1524.5101 | 1536.5706 | 1548.0397 | 1576.734
nuclear | 806.9683 | 790.2044 | 769.3312 | 789.0165 | 797.166 | 797.1779 | 805.6939 | 804.9496 | 807.0845 | 809.4093 | 789.9186 | 777.6822 | 783.6156 | 785.4799 | 788.973 | 781.7759 | 773.3351 | 759.4032 | 690.6391 | 691.0634 | 684.0129 | 685.1061 | 680.9739 | 623.6688 | 589.5201 | 571.7114 | 563.7052 | 556.5094 | 539.3662 | 531.6991 | 532.0439 | 483.8661 | 484.7721 | 485.5721 | 448.5472 | 428.5564 | 411.8517 | 392.0768 | 367.1768 | 356.4677 | 336.9998
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
coal | 1847.2903 | 1733.43 | 1514.0429 | 1581.1147 | 1581.7103 | 1352.3982 | 1239.1487 | 1205.8353 | 1149.4873 | 964.9568 | 773.8053 | 954.065 | 918.9 | 882.3397 | 771.8292 | 755.281 | 742.5298 | 738.535 | 738.0948 | 733.0863 | 709.3178 | 701.4343 | 703.1122 | 703.1851 | 676.6197 | 663.2624 | 650.2139 | 650.1903 | 642.8788 | 633.6414 | 622.9826 | 621.3544 | 615.4145 | 607.7131 | 601.8514 | 591.4052 | 588.8148 | 588.2515 | 584.1076 | 583.8239 | 573.4067
renewables | 427.3761 | 513.3361 | 494.5732 | 522.0734 | 538.5793 | 544.241 | 609.4451 | 686.5827 | 706.8158 | 728.6727 | 792.4961 | 878.7213 | 972.8674 | 1059.7399 | 1152.4265 | 1233.6017 | 1273.4552 | 1311.1948 | 1345.6125 | 1371.7676 | 1417.748 | 1442.2609 | 1456.5038 | 1471.6111 | 1507.5311 | 1553.374 | 1581.4404 | 1604.2439 | 1621.817 | 1639.5013 | 1659.6106 | 1683.8696 | 1712.7465 | 1742.4691 | 1778.1144 | 1814.5334 | 1847.1493 | 1877.1049 | 1903.2041 | 1930.2234 | 1960.8254
natural gas | 987.6972 | 1013.6889 | 1225.8942 | 1124.8356 | 1126.609 | 1333.4821 | 1378.3069 | 1296.4425 | 1469.1327 | 1585.8142 | 1616.748 | 1563.9108 | 1525.282 | 1574.479 | 1617.4059 | 1593.9937 | 1603.7837 | 1605.9307 | 1630.9774 | 1636.9948 | 1637.5522 | 1649.6324 | 1661.7874 | 1700.2417 | 1721.8644 | 1725.6644 | 1750.7745 | 1772.3815 | 1807.0428 | 1841.8633 | 1873.1626 | 1897.7012 | 1923.4272 | 1950.8724 | 1970.8281 | 1995.5945 | 2017.6875 | 2041.4546 | 2073.9229 | 2105.7161 | 2144.5918
nuclear | 806.9683 | 790.2044 | 769.3312 | 789.0165 | 797.166 | 797.1779 | 805.6939 | 804.9496 | 807.0845 | 809.4093 | 789.9186 | 777.6822 | 783.6156 | 785.4799 | 788.9731 | 781.776 | 773.3351 | 759.4032 | 721.8088 | 722.2331 | 722.9515 | 724.0448 | 724.8032 | 700.3097 | 701.0043 | 702.4093 | 703.4539 | 703.6646 | 703.8752 | 703.8756 | 704.2205 | 705.4722 | 706.3782 | 707.2517 | 708.007 | 708.8251 | 709.2521 | 709.6777 | 709.943 | 710.2641 | 710.7277
U.S. electricity generation, AEO2022 renewables cost cases

## Slide 40: Installed electric generating capacity by source
other diurnal storage solar wind nuclear oil and natural gas coal
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
 | 301.1162 | 215.6721 | 124.4972 | 108.532 | 105.5947
 | 479.6735 | 506.4893 | 629.2366 | 743.7663 | 869.8042
 | 103.7491 | 96.5236 | 86.0359 | 81.0193 | 80.6239
 | 39.8813 | 118.3265 | 187.7809 | 210.634 | 229.4532
 | 2.6498 | 82.2411 | 286.9896 | 432.2074 | 580.0067
 | 0.019 | 1.2123 | 15.0303 | 19.7763 | 27.7065
 | 115.9863 | 117.8966 | 120.4307 | 123.9149 | 126.3292
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
 | 301.1162 | 215.6721 | 124.4972 | 108.532 | 105.5947
 | 479.6735 | 506.4893 | 629.2366 | 743.7663 | 869.8042
 | 103.7491 | 96.5236 | 86.0359 | 81.0193 | 80.6239
 | 39.8813 | 118.3265 | 187.7809 | 210.634 | 229.4532
 | 2.6498 | 82.2411 | 286.9896 | 432.2074 | 580.0067
 | 0.019 | 1.2123 | 15.0303 | 19.7763 | 27.7065
 | 115.9863 | 117.8966 | 120.4307 | 123.9149 | 126.3292

## Slide 41: U.S. retiring and new generating capacity
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
nuclear | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1.122 | 0 | 0 | 0 | 0 | 0 | 2.228 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
coal | 0.3994 | 0.5309 | 1.4189 | 1.4582 | 1.7863 | 5.3443 | 3.8303 | 3.734 | 1.5276 | 0 | 0 | 0 | 0 | 0 | 0 | 0.017 | 0 | 0.000383 | 0.000715 | 0 | 0 | 0.001 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
oil and gas | 15.5681 | 9.431 | 7.077 | 7.8143 | 9.5344 | 7.5118 | 10.261 | 9.7267 | 7.1602 | 9.0993 | 6.4699 | 8.6817 | 9.6405 | 19.3251 | 7.9735 | 6.403 | 6.2688 | 22.0756 | 19.9109 | 17.223 | 25.1806 | 12.6927 | 21.8542 | 9.4415 | 17.8439 | 8.2922 | 9.005 | 12.8108 | 15.5822 | 15.2909 | 14.323 | 12.1347 | 10.3962 | 13.0986 | 10.7286 | 10.6888 | 13.4847 | 9.2861 | 10.2745 | 16.1238 | 10.4119 | 11.432 | 14.0131 | 11.1684 | 18.9809 | 14.4061
other | 0.115 | 0.3324 | 0.3863 | 0.422 | 0.515 | 0.3971 | 0.6273 | 1.0152 | 1.3316 | 0.4639 | 0.5769 | 0.6966 | 0.5258 | 0.5434 | 0.4273 | 0.7412 | 4.5951 | 2.7011 | 2.2888 | 0.90228 | 1.3047 | 0.92614 | 1.6299 | 2.2692 | 0.88512 | 0.87444 | 0.64646 | 2.0632 | 0.55435 | 0.63529 | 1.4265 | 0.48453 | 0.39161 | 0.4158 | 1.2575 | 0.35611 | 1.1951 | 0.95757 | 2.123 | 0.98032 | 0.50434 | 0.83361 | 0.37858 | 0.4554 | 2.3504 | 0.56571
wind | 2.1622 | 2.6545 | 5.2999 | 8.4848 | 9.9198 | 4.6639 | 6.839 | 13.25 | 0.8644 | 4.9557 | 8.2383 | 8.7498 | 6.0625 | 6.8882 | 9.2672 | 14.6649 | 17.1942 | 6.9366 | 3.5172 | 5.825 | 18.7962 | 3.4401 | 0.78364 | 2.496 | 3.0804 | 7.3865 | 0.30543 | 0.39277 | 0.59832 | 5.8291 | 8.8694 | 1.0962 | 2.5056 | 0.58345 | 0.79306 | 1.9723 | 1.1516 | 2.4888 | 3.3276 | 0.55867 | 1.4351 | 2.6412 | 1.4359 | 1.2134 | 1.746 | 2.9644
solar | 0.60962 | 0.19535 | 0.23726 | 0.3147 | 0.41088 | 0.88195 | 1.7824 | 3.2469 | 5.2139 | 5.9998 | 6.3931 | 12.0883 | 9.6946 | 9.2956 | 10.3405 | 15.5362 | 21.0109 | 22.632 | 32.9815 | 40.4273 | 10.9486 | 11.0388 | 10.3648 | 16.3501 | 27.6543 | 11.2021 | 12.6112 | 11.8441 | 21.7435 | 18.8249 | 13.7244 | 18.1895 | 11.9887 | 10.8283 | 13.893 | 11.2952 | 9.7764 | 11.6592 | 14.1638 | 11.0202 | 14.632 | 14.3889 | 16.428 | 21.6926 | 18.5093 | 15.0783
nuclear | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -3.576 | -0.6124 | 0 | -0.4828 | 0 | -0.6077 | -1.4764 | -1.6129 | -1.0363 | -0.7685 | 0 | 0 | -1.122 | -1.118 | -2.171 | -4.7739 | -0.9845 | -1.168 | 0 | 0 | -5.007 | 0 | 0 | 0 | -0.8333 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -1.225 | 0 | 0
coal | -0.2723 | -0.7538 | -1.241 | -0.7944 | -0.5481 | -1.4845 | -2.7388 | -10.4315 | -6.0615 | -4.2952 | -14.8664 | -7.9059 | -6.3097 | -13.3042 | -12.9026 | -10.4567 | -4.5704 | -9.8133 | -8.991 | -6.9201 | -19.8898 | -6.806 | -6.5148 | -11.1707 | -10.9953 | -4.985 | -0.81701 | -2.516 | -0.762 | -5.27 | -1.616 | -1.004 | -0.713 | -1.067 | -0.339 | -1.765 | -0.34 | 0 | 0 | 0 | -2.514 | 0 | 0 | 0 | 0 | 0
oil and gas | -3.7135 | -2.8338 | -3.5008 | -1.7772 | -5.0687 | -3.6614 | -3.6597 | -5.7842 | -8.1608 | -5.2363 | -7.084 | -9.0083 | -5.4057 | -8.8748 | -4.6119 | -3.8097 | -1.2586 | -3.0217 | -7.9093 | -9.7906 | -7.0144 | -3.52 | -2.7401 | -0.7758 | -1.4693 | -0.6755 | -1.167 | -1.623 | -0.9609 | -0.548 | -1.8915 | -1.4 | -1.294 | -0.003 | 0 | -0.641 | -0.209 | -0.5599 | -0.023099 | -0.6851 | -0.1269 | 0 | -0.0566 | -0.1255 | -1.3886 | -0.398
other | -0.1325 | -0.2333 | -0.1314 | -0.0763 | -0.1673 | -0.3674 | -0.2894 | -0.5848 | -0.342 | -0.3633 | -0.547 | -0.3598 | -0.3011 | -0.387 | -0.9278 | -0.1988 | -0.1848 | -0.0121 | -0.0214 | -0.0198 | -0.0829 | -0.0516 | -0.0629 | -0.2873 | -0.1395 | -0.018 | -0.0112 | 0 | -0.043 | -0.0383 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -0.0914 | -0.05 | -0.0026 | -0.003 | 0 | -0.015 | -0.002
Annual electricity generating capacity additions and retirements
AEO2022 Reference case
gigawatts
Source: Form EIA-860M, Monthly Update to the Annual Electric Generator Report, August 2021

## Slide 42: Electricity prices by components and long-term average electricity prices
Chart: 
| 2020 | 2030 | 2040 | 2050
generation | 6.5507 | 5.4935 | 5.1505 | 4.8396
transmission | 1.4215 | 1.5755 | 1.6806 | 1.6847
distribution | 3.0181 | 3.4701 | 3.6562 | 3.6693
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Low Oil and Gas Supply | 12.0746 | 11.9119 | 11.6169 | 11.6834 | 11.8926 | 11.7466 | 11.4683 | 11.4868 | 11.271 | 11.0838 | 11.0758 | 11.0884 | 10.9498 | 11.0582 | 10.9811 | 10.9981 | 11.0899 | 11.1376 | 11.2301 | 11.315 | 11.3858 | 11.4615 | 11.5327 | 11.6336 | 11.6679 | 11.6226 | 11.6484 | 11.6441 | 11.6577 | 11.6506 | 11.6819 | 11.6893 | 11.6248 | 11.5662 | 11.5859 | 11.5632 | 11.5881 | 11.5541 | 11.518 | 11.537 | 11.4913
High Oil and Gas Supply | 12.0746 | 11.9119 | 11.6169 | 11.6834 | 11.8926 | 11.7466 | 11.4683 | 11.4868 | 11.271 | 11.0838 | 11.0758 | 11.0762 | 10.9543 | 10.6302 | 10.3229 | 10.2186 | 10.2105 | 10.1954 | 10.1891 | 10.1779 | 10.1279 | 10.1755 | 10.1527 | 10.1653 | 10.1883 | 10.0931 | 10.076 | 10.0485 | 9.9875 | 9.9702 | 9.9885 | 9.9414 | 9.9224 | 9.8941 | 9.8457 | 9.8307 | 9.8442 | 9.7797 | 9.7796 | 9.7533 | 9.7005
Low Ren | 12.0746 | 11.9119 | 11.6169 | 11.6834 | 11.8926 | 11.7466 | 11.4683 | 11.4868 | 11.271 | 11.0838 | 11.0758 | 11.0763 | 10.9518 | 10.7695 | 10.531 | 10.4463 | 10.4322 | 10.4425 | 10.4817 | 10.528 | 10.5401 | 10.5905 | 10.5619 | 10.5818 | 10.6068 | 10.5234 | 10.4924 | 10.4793 | 10.4253 | 10.3996 | 10.4248 | 10.3968 | 10.3459 | 10.3435 | 10.2776 | 10.2628 | 10.2221 | 10.1442 | 10.1475 | 10.0987 | 10.0066
High Ren | 12.0746 | 11.9119 | 11.6169 | 11.6834 | 11.8926 | 11.7466 | 11.4683 | 11.4868 | 11.271 | 11.0838 | 11.0758 | 11.075 | 10.9527 | 10.7668 | 10.5683 | 10.521 | 10.5027 | 10.5405 | 10.6149 | 10.6288 | 10.628 | 10.6993 | 10.7102 | 10.7914 | 10.8004 | 10.7373 | 10.7137 | 10.6912 | 10.6614 | 10.6917 | 10.7099 | 10.6831 | 10.6655 | 10.644 | 10.6132 | 10.6211 | 10.609 | 10.5997 | 10.5949 | 10.5536 | 10.5167
Reference | 12.0746 | 11.9119 | 11.6169 | 11.6834 | 11.8926 | 11.7466 | 11.4683 | 11.4868 | 11.271 | 11.0838 | 11.0758 | 11.0757 | 11.0094 | 10.8037 | 10.5356 | 10.4776 | 10.4459 | 10.468 | 10.5066 | 10.5373 | 10.5529 | 10.5888 | 10.6078 | 10.6663 | 10.7025 | 10.639 | 10.6159 | 10.5602 | 10.5049 | 10.5086 | 10.502 | 10.4607 | 10.4498 | 10.4213 | 10.3463 | 10.3446 | 10.3261 | 10.2953 | 10.3084 | 10.2845 | 10.2101

## Slide 43: U.S. electricity generation by source
Hourly U.S. electricity generation and load by fuel for selected cases and representative years
billion kilowatthours
AEO2022 Reference case, 2021 AEO2022 Reference case, 2050 AEO2022 Low Renewables Cost case, 2050
hour of the day
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Coal | 26.8982 | 26.6615 | 25.8916 | 25.8716 | 27.2938 | 30.6331 | 35.2277 | 38.1864 | 39.6289 | 40.4584 | 40.8877 | 41.1943 | 41.2916 | 41.3534 | 41.3893 | 41.8287 | 42.7118 | 43.76 | 43.8305 | 43.252 | 42.404 | 40.2987 | 36.9423 | 33.1163
Nuclear | 32.8337 | 32.8462 | 32.8117 | 32.8033 | 32.8245 | 32.9011 | 33.0205 | 33.0962 | 33.1336 | 33.1671 | 33.1914 | 33.2066 | 33.2146 | 33.2172 | 33.2118 | 33.211 | 33.2163 | 33.2387 | 33.2427 | 33.2418 | 33.2151 | 33.1715 | 33.0777 | 32.982
Oil and Gas Peakers | 1.9477 | 1.8108 | 1.6048 | 1.5617 | 1.7219 | 2.16 | 3.1979 | 4.1589 | 4.587 | 4.8533 | 5.1019 | 5.3651 | 5.5524 | 5.6566 | 5.9046 | 5.8944 | 6.0922 | 6.3414 | 6.2645 | 5.9162 | 5.4847 | 4.9506 | 4.1483 | 3.1729
Gas Combined-Cycle | 50.2029 | 49.824 | 48.8565 | 48.595 | 49.1342 | 51.1224 | 54.5737 | 56.939 | 57.4444 | 58.4769 | 59.5428 | 60.459 | 61.1662 | 61.6824 | 62.2566 | 63.6236 | 65.4219 | 66.8531 | 66.968 | 66.0502 | 64.7874 | 62.4427 | 58.7694 | 55.0716
Hydro | 7.0108 | 7.3153 | 6.8196 | 6.9654 | 7.574 | 9.421 | 11.9648 | 12.3018 | 11.0916 | 10.4996 | 10.236 | 10.3937 | 10.549 | 10.6484 | 10.6845 | 11.2883 | 12.7323 | 14.8587 | 15.3579 | 15.2058 | 14.3329 | 12.2211 | 9.7695 | 7.7486
Wind | 18.2969 | 18.1704 | 17.9439 | 17.6658 | 17.3636 | 17.0167 | 16.0386 | 14.2916 | 12.5981 | 11.1846 | 10.5648 | 10.5047 | 10.7274 | 11.1579 | 11.6406 | 12.1226 | 12.6879 | 13.5062 | 14.7315 | 16.3357 | 17.5748 | 18.1925 | 18.4075 | 18.395
Solar Hybrid | 0.00022681 | 0.00048718 | 0.00029628 | 0.00021602 | 0.00044661 | 0.0324 | 0.12412 | 0.2249 | 0.29764 | 0.29557 | 0.29374 | 0.30431 | 0.32513 | 0.34131 | 0.35113 | 0.3584 | 0.33171 | 0.28193 | 0.18082 | 0.10776 | 0.043759 | 0.0044883 | 0.001161 | 0.00041043
Solar | 0.0030551 | 0.16216 | 1.3162 | 5.3923 | 10.8895 | 15.3556 | 17.5714 | 18.3197 | 18.3211 | 17.6746 | 15.6938 | 11.6773 | 6.4839 | 2.0205 | 0.31446 | 0.014665 | 3.728e-05
Curtailment | 0.018485 | 0.030084 | 0.13048 | 0.15797 | 0.16463 | 0.15136 | 0.077744 | 0.021202
Pumped Hydro discharge | 0.015058 | 0.07351 | 0.050288 | 0.054627 | 0.111 | 0.24274 | 0.43211 | 0.35629 | 0.32739 | 0.36014 | 0.3847 | 0.3739 | 0.3893 | 0.48776 | 0.57712 | 0.78555 | 1.1526 | 1.797 | 1.899 | 1.861 | 1.7356 | 1.0454 | 0.37491 | 0.10083
Battery Storage discharge | 0.021695 | 0.01274 | 0.005814 | 0.01477 | 0.054284 | 0.12388 | 0.14183 | 0.045208 | 0.023304 | 0.051655 | 0.035288 | 0.028834 | 0.035124 | 0.029743 | 0.048087 | 0.044202 | 0.14014 | 0.29454 | 0.29146 | 0.28791 | 0.23059 | 0.2083 | 0.087977 | 0.043688
Pumped Hydro charge | -1.4329 | -1.4673 | -1.8289 | -1.9342 | -1.7813 | -1.2334 | -0.60752 | -0.46063 | -0.64665 | -0.81294 | -0.82917 | -0.83736 | -0.85479 | -0.83121 | -0.69129 | -0.40812 | -0.03828 | -0.0071821 | -0.011825 | -0.02573 | -0.028966 | -0.054051 | -0.27972 | -0.9543
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Coal | 25.7696 | 25.8709 | 25.4072 | 25.0853 | 24.8419 | 25.3585 | 25.5766 | 24.856 | 23.3611 | 21.1848 | 19.4756 | 18.6306 | 18.5382 | 19.2424 | 20.8645 | 23.1049 | 25.3716 | 27.5463 | 28.4738 | 28.6935 | 28.4766 | 27.7914 | 27.2888 | 26.8272
Nuclear | 27.1592 | 27.1794 | 27.1126 | 27.0674 | 27.0033 | 27.0399 | 27.1352 | 27.1933 | 26.8007 | 25.5657 | 23.8888 | 22.615 | 22.5248 | 23.5379 | 25.0026 | 26.2204 | 27.0443 | 27.4264 | 27.4951 | 27.4665 | 27.4293 | 27.3629 | 27.317 | 27.2792
Oil and Gas Peakers | 0.42964 | 0.33395 | 0.25358 | 0.20962 | 0.18844 | 0.21558 | 0.26741 | 0.25768 | 0.22353 | 0.15305 | 0.13321 | 0.12971 | 0.14688 | 0.16885 | 0.32198 | 0.8182 | 1.603 | 3.8595 | 5.7254 | 5.1128 | 4.0335 | 2.7212 | 1.7255 | 0.94345
Gas Combined-Cycle | 77.4797 | 76.4758 | 72.1682 | 69.4077 | 67.0148 | 68.3765 | 69.3505 | 61.8394 | 46.1217 | 34.3417 | 30.5698 | 30.7713 | 32.5422 | 34.9846 | 40.707 | 53.2412 | 73.6702 | 96.7591 | 104.4745 | 103.2293 | 100.824 | 96.192 | 92.1022 | 88.5743
Hydro | 15.3396 | 16.0088 | 14.7851 | 13.9824 | 12.8262 | 14.4953 | 14.9235 | 10.9603 | 8.4802 | 6.7127 | 5.9644 | 5.8513 | 5.7672 | 5.9482 | 6.4483 | 8.2676 | 11.625 | 16.0966 | 17.3313 | 16.9819 | 16.6619 | 15.8352 | 15.2947 | 14.4623
Wind | 36.6422 | 36.3125 | 35.8646 | 35.3248 | 34.7711 | 34.1574 | 32.298 | 29.0388 | 25.7407 | 22.0628 | 20.4645 | 20.8277 | 21.5243 | 22.2992 | 23.1127 | 25.0092 | 27.763 | 29.768 | 31.7042 | 34.1878 | 36.0416 | 36.865 | 37.0687 | 36.9165
Solar Hybrid | 0.010979 | 0.0088286 | 0.0064163 | 0.0038042 | 0.010327 | 0.83957 | 4.4197 | 10.1186 | 14.9519 | 16.0148 | 15.1078 | 14.8073 | 15.2499 | 16.235 | 17.3558 | 18.7747 | 18.2028 | 15.7019 | 10.1047 | 5.6586 | 2.5988 | 0.27304 | 0.074011 | 0.023085
Solar | 0.010888 | 0.84257 | 7.474 | 32.9051 | 70.4674 | 101.228 | 121.0012 | 129.6751 | 130.6287 | 126.1232 | 113.366 | 87.0931 | 51.1969 | 17.2201 | 2.669 | 0.13698 | 0.00021537
Curtailment | 0.027833 | 0.0018711 | 0.0058653 | 0.010304 | 0.0040905 | 0.062191 | 0.90952 | 2.9098 | 6.7524 | 7.7077 | 6.3116 | 5.9911 | 5.9802 | 5.2862 | 2.6567 | 0.58836 | 0.0045349
Pumped Hydro discharge | 1.707 | 1.4232 | 0.54336 | 0.56012 | 0.36971 | 0.5777 | 0.80849 | 0.59684 | 0.15404 | 0.035782 | 0.0084935 | 0.0092473 | 0.16783 | 1.5306 | 4.2729 | 4.8735 | 4.9143 | 4.6069 | 3.328 | 2.1715 | 1.3687
Battery Storage discharge | 1.9816 | 1.855 | 0.88309 | 0.25506 | 0.15735 | 0.21682 | 0.7356 | 0.73464 | 0.10876 | 0.022778 | 0.010366 | 0.032271 | 0.0088542 | 0.0087662 | 0.047889 | 0.12525 | 1.2266 | 5.4403 | 6.8774 | 6.042 | 4.8976 | 2.6262 | 1.4515 | 1.2895
Pumped Hydro charge | -0.22214 | -0.14551 | -0.28015 | -0.42354 | -0.62387 | -0.34711 | -0.60412 | -1.9281 | -2.924 | -4.4877 | -5.1457 | -5.259 | -5.2423 | -4.8373 | -4.2988 | -2.7542 | -1.0015 | -0.11889 | -0.018488 | -0.0099686 | -0.035719 | -0.081187 | -0.20863
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Coal | 18.7322 | 18.8095 | 18.5261 | 18.3527 | 18.1945 | 18.4034 | 17.9494 | 16.6743 | 14.984 | 13.4685 | 12.62 | 12.1815 | 12.0248 | 12.2842 | 13.2809 | 15.0334 | 17.1072 | 19.4197 | 20.6077 | 20.9549 | 20.9237 | 20.4489 | 20.0479 | 19.7561
Nuclear | 14.6669 | 14.6612 | 14.6376 | 14.6236 | 14.608 | 14.6217 | 14.6066 | 14.3027 | 13.277 | 12.0208 | 10.7614 | 9.8953 | 9.9436 | 10.646 | 11.8021 | 13.0261 | 14.0585 | 14.7062 | 14.8234 | 14.8195 | 14.8023 | 14.7576 | 14.7254 | 14.7047
Oil and Gas Peakers | 0.45039 | 0.40568 | 0.3465 | 0.2597 | 0.21791 | 0.25907 | 0.25778 | 0.17199 | 0.1547 | 0.043916 | 0.029459 | 0.019336 | 0.016736 | 0.015879 | 0.019822 | 0.21199 | 0.60131 | 1.69 | 2.1657 | 2.0349 | 1.9208 | 1.7186 | 1.3036 | 0.95169
Gas Combined-Cycle | 68.0408 | 67.706 | 65.4583 | 63.6572 | 61.7635 | 62.3392 | 60.1205 | 46.508 | 29.3364 | 22.6576 | 21.1988 | 21.0532 | 21.3999 | 22.1227 | 24.6367 | 33.721 | 54.8392 | 76.3163 | 84.0407 | 83.9499 | 83.0354 | 81.0815 | 78.6758 | 76.4137
Hydro | 16.1205 | 16.9988 | 16.2736 | 15.7037 | 14.9488 | 16.2203 | 15.6895 | 10.9689 | 7.4893 | 5.6322 | 4.9919 | 4.8886 | 5.1121 | 5.3797 | 5.8136 | 6.9615 | 10.4839 | 13.9933 | 15.5844 | 15.561 | 16.0893 | 16.4469 | 16.5453 | 16.2408
Wind | 58.5606 | 57.8597 | 57.0615 | 56.151 | 55.2102 | 54.1839 | 50.9248 | 45.2569 | 39.6364 | 33.773 | 31.7175 | 32.7127 | 34.5093 | 36.0006 | 37.7607 | 40.4795 | 43.4211 | 46.5644 | 50.0698 | 54.3893 | 57.6014 | 59.0021 | 59.3711 | 59.0725
Solar Hybrid | 0.020344 | 0.015501 | 0.0106 | 0.0068151 | 0.018282 | 1.5036 | 8.0101 | 18.1205 | 26.1714 | 28.219 | 26.9236 | 27.0819 | 27.9116 | 29.6513 | 31.6342 | 33.0081 | 31.2164 | 26.6495 | 17.0131 | 9.4231 | 4.2796 | 0.48177 | 0.13664 | 0.049992
Solar | 0.01281 | 1.1259 | 9.9277 | 43.0776 | 90.5096 | 127.3668 | 154.5008 | 167.9149 | 169.3085 | 163.7165 | 147.0102 | 112.1691 | 65.3812 | 21.5966 | 3.339 | 0.16297 | 0.0002629
Curtailment | 0.00051663 | 0.28257 | 2.1143 | 6.5236 | 14.8078 | 14.39 | 9.7711 | 8.602 | 7.4651 | 4.8219 | 2.1674 | 0.80363 | 0.11273
Pumped Hydro discharge | 2.089 | 2.3649 | 1.5752 | 1.2985 | 1.045 | 1.32 | 0.86432 | 0.58499 | 0.050406 | 0.00057125 | 0.039452 | 1.482 | 4.0221 | 4.455 | 4.5937 | 4.3443 | 3.5961 | 3.3556 | 2.8644
Battery Storage discharge | 8.3952 | 6.6767 | 3.6345 | 2.5633 | 1.8021 | 2.5236 | 4.5572 | 3.1244 | 0.36315 | 0.048673 | 0.071758 | 0.082065 | 0.034814 | 0.022477 | 0.015581 | 0.28989 | 4.0638 | 20.8094 | 29.3072 | 28.1967 | 23.922 | 17.1104 | 11.4752 | 8.3932
Pumped Hydro charge | -0.079679 | -0.073189 | -0.12661 | -0.17244 | -0.23995 | -0.1314 | -0.48356 | -2.0538 | -4.2575 | -5.8684 | -6.1258 | -6.0453 | -5.9722 | -5.6149 | -5.327 | -4.1282 | -1.2283 | -0.085115 | -0.0069012 | -0.008014 | -0.0054132 | -0.023389 | -0.070318
curtailment battery storage pumped storage solar wind hydroelectric natural gas combined-cycle natural gas and oil peakers nuclear coal
Note: Negative generation represents charging of energy storage technologies such as pumped hydro and battery storage. Hourly dispatch estimates are illustrative and are developed to determine curtailment and storage operations; final dispatch estimates are developed separately and may differ from total utilization as this figure shows. Solar includes both utility-scale and end-use photovoltaic electricity generation

## Slide 44: Transportation sector energy consumption
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
other | 1.7441 | 1.735 | 1.6648 | 1.5452 | 1.6274 | 1.6492 | 1.6031 | 1.5563 | 1.6783 | 1.7093 | 1.6328 | 1.5864 | 1.5732 | 1.5622 | 1.5556 | 1.5518 | 1.5459 | 1.532 | 1.5393 | 1.5341 | 1.5282 | 1.5249 | 1.529 | 1.5289 | 1.5261 | 1.5274 | 1.5307 | 1.5392 | 1.5464 | 1.5508 | 1.5587 | 1.5659 | 1.5688 | 1.5773 | 1.58 | 1.5837 | 1.5911 | 1.5986 | 1.6057 | 1.6088 | 1.6151
marine | 1.2898 | 1.1708 | 1.0294 | 0.9851 | 0.89555 | 0.95717 | 1.1388 | 1.173 | 1.1216 | 1.0697 | 1.1147 | 1.2067 | 1.2754 | 1.169 | 1.1682 | 1.1688 | 1.1648 | 1.1574 | 1.1527 | 1.1499 | 1.1462 | 1.149 | 1.147 | 1.1459 | 1.1452 | 1.1443 | 1.1442 | 1.1446 | 1.1426 | 1.1426 | 1.1367 | 1.134 | 1.1315 | 1.1266 | 1.1232 | 1.1224 | 1.1205 | 1.119 | 1.1188 | 1.1185 | 1.1192
rail | 0.4706 | 0.53782 | 0.50046 | 0.51235 | 0.54335 | 0.52432 | 0.46456 | 0.49626 | 0.53314 | 0.50979 | 0.46668 | 0.504 | 0.51142 | 0.51761 | 0.48847 | 0.49693 | 0.50732 | 0.50762 | 0.50737 | 0.50679 | 0.50748 | 0.50856 | 0.50951 | 0.51088 | 0.50694 | 0.50576 | 0.50174 | 0.50285 | 0.50304 | 0.50318 | 0.50274 | 0.50281 | 0.50356 | 0.50282 | 0.50157 | 0.50124 | 0.50184 | 0.50142 | 0.50153 | 0.50226 | 0.50522
commercial light trucks | 0.71996 | 0.74687 | 0.75403 | 0.78807 | 0.81049 | 0.8369 | 0.85501 | 0.86024 | 0.89354 | 0.89144 | 0.83465 | 0.88832 | 0.90756 | 0.91529 | 0.91475 | 0.91748 | 0.91796 | 0.91472 | 0.91314 | 0.91295 | 0.91362 | 0.91489 | 0.91747 | 0.92115 | 0.92548 | 0.93015 | 0.93585 | 0.94334 | 0.95109 | 0.959 | 0.96711 | 0.97633 | 0.98592 | 0.9965 | 1.007 | 1.0178 | 1.0306 | 1.0412 | 1.0505 | 1.0614 | 1.0748
air | 2.6082 | 2.6658 | 2.6532 | 2.7052 | 2.7502 | 2.8746 | 2.9941 | 3.0741 | 3.188 | 3.1841 | 1.9078 | 2.2962 | 2.6837 | 2.9511 | 3.0347 | 3.1117 | 3.174 | 3.214 | 3.2521 | 3.2938 | 3.3404 | 3.3773 | 3.3935 | 3.4312 | 3.4652 | 3.5015 | 3.5384 | 3.5807 | 3.6192 | 3.6637 | 3.713 | 3.7538 | 3.7994 | 3.8472 | 3.8925 | 3.9457 | 3.999 | 4.0457 | 4.091 | 4.1441 | 4.2032
medium and heavy duty | 5.1041 | 5.1501 | 4.9918 | 5.1339 | 5.3243 | 5.3696 | 5.3885 | 5.4825 | 5.6752 | 5.6771 | 5.352 | 5.5674 | 5.6474 | 5.6688 | 5.6632 | 5.6559 | 5.6286 | 5.5797 | 5.5408 | 5.504 | 5.4627 | 5.4218 | 5.386 | 5.3561 | 5.3297 | 5.3121 | 5.3005 | 5.3 | 5.305 | 5.3128 | 5.3245 | 5.3442 | 5.3719 | 5.3998 | 5.43 | 5.4619 | 5.4986 | 5.5262 | 5.5455 | 5.579 | 5.6264
light-duty vehicles | 15.1322 | 14.7085 | 14.6138 | 14.8004 | 14.9605 | 15.0665 | 15.3415 | 15.2534 | 15.2794 | 15.263 | 13.1424 | 14.2745 | 14.6631 | 14.9074 | 14.8888 | 14.8492 | 14.7869 | 14.6994 | 14.5962 | 14.5048 | 14.4394 | 14.3889 | 14.3282 | 14.2939 | 14.2639 | 14.2295 | 14.2037 | 14.1925 | 14.1882 | 14.1976 | 14.2177 | 14.24 | 14.2684 | 14.3019 | 14.3452 | 14.3996 | 14.4682 | 14.5404 | 14.6166 | 14.702 | 14.7994
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
other | 1.8347 | 1.7236 | 1.5991 | 1.4846 | 1.4532 | 1.476 | 1.6324 | 1.6627 | 1.7405 | 1.6806 | 1.5566 | 1.6487 | 1.8059 | 1.6062 | 1.623 | 1.6467 | 1.6642 | 1.6694 | 1.6993 | 1.7261 | 1.747 | 1.7839 | 1.82 | 1.8514 | 1.8813 | 1.916 | 1.9541 | 1.999 | 2.0385 | 2.0796 | 2.1142 | 2.1531 | 2.1881 | 2.227 | 2.2631 | 2.303 | 2.3468 | 2.3911 | 2.4363 | 2.4796 | 2.5284
electricity | 0.024003 | 0.025379 | 0.025105 | 0.026959 | 0.028288 | 0.029765 | 0.031406 | 0.033147 | 0.036557 | 0.04064 | 0.033789 | 0.044181 | 0.056331 | 0.069239 | 0.082837 | 0.096995 | 0.11166 | 0.12627 | 0.14064 | 0.15507 | 0.16984 | 0.18491 | 0.19989 | 0.21512 | 0.2305 | 0.2459 | 0.26146 | 0.27729 | 0.29327 | 0.30944 | 0.32581 | 0.34209 | 0.35838 | 0.37503 | 0.39202 | 0.40922 | 0.42637 | 0.44357 | 0.46086 | 0.47859 | 0.49707
jet fuel | 3.1427 | 3.1645 | 3.118 | 3.1076 | 3.1393 | 3.2812 | 3.3859 | 3.4412 | 3.5345 | 3.5489 | 2.2873 | 2.6759 | 3.1316 | 3.4736 | 3.5601 | 3.6427 | 3.7093 | 3.7521 | 3.7931 | 3.8352 | 3.8847 | 3.9223 | 3.939 | 3.978 | 4.0131 | 4.0506 | 4.0887 | 4.1326 | 4.1725 | 4.2187 | 4.2698 | 4.3121 | 4.3594 | 4.4089 | 4.4559 | 4.511 | 4.5663 | 4.6147 | 4.6618 | 4.717 | 4.7786
distillate fuel oil | 5.826 | 5.9997 | 5.7383 | 5.8984 | 6.1587 | 6.255 | 6.2022 | 6.2529 | 6.5547 | 6.5723 | 6.2777 | 6.4964 | 6.4785 | 6.6075 | 6.5706 | 6.5628 | 6.5386 | 6.486 | 6.4383 | 6.3873 | 6.3349 | 6.2794 | 6.2298 | 6.1865 | 6.1404 | 6.1031 | 6.0682 | 6.0459 | 6.0312 | 6.0166 | 6.0084 | 6.0048 | 6.0084 | 6.0113 | 6.0125 | 6.0153 | 6.0225 | 6.0202 | 6.0095 | 6.0106 | 6.025
motor gasoline | 16.3334 | 15.8941 | 15.8104 | 16.0384 | 16.2159 | 16.3201 | 16.6198 | 16.5981 | 16.5989 | 16.5599 | 14.3538 | 15.5345 | 15.9507 | 16.2084 | 16.1796 | 16.1315 | 16.0571 | 15.9516 | 15.8345 | 15.7323 | 15.6571 | 15.5967 | 15.529 | 15.489 | 15.4545 | 15.4169 | 15.3893 | 15.3801 | 15.3778 | 15.39 | 15.4135 | 15.442 | 15.4787 | 15.5205 | 15.5731 | 15.6379 | 15.7195 | 15.8025 | 15.8881 | 15.9867 | 16.1008
Transportation sector consumption by fuel
AEO2022 Reference case
quadrillion British thermal units
Transportation sector consumption by mode
AEO2022 Reference case
quadrillion British thermal units
light-duty
vehicles
medium- and
heavy-duty
vehicles
air
commercial
light trucks
rail
marine
other

## Slide 45: Transportation sector delivered electricity and natural gas
Chart: 
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
light-duty vehicles | 17.1277 | 24.7647 | 34.5131 | 45.9203 | 58.1851 | 71.2851 | 85.0341 | 98.9747 | 112.7834 | 126.6797 | 140.8305 | 155.2828 | 169.7338 | 184.4348 | 199.3291 | 214.2976 | 229.4014 | 244.7263 | 260.2013 | 275.8972 | 291.7035 | 307.4797 | 323.225 | 339.265 | 355.5965 | 372.0571 | 388.3423 | 404.6612 | 420.9527 | 437.3862 | 454.0436
passenger rail | 20.8347 | 24.4509 | 27.754 | 29.9509 | 31.8219 | 33.2941 | 34.528 | 35.4478 | 36.1964 | 36.8803 | 37.6113 | 38.3128 | 38.9038 | 39.4643 | 39.9681 | 40.3951 | 40.8284 | 41.2871 | 41.7319 | 42.1277 | 42.5922 | 42.9826 | 43.3755 | 43.8109 | 44.2501 | 44.7222 | 45.2483 | 45.698 | 46.1234 | 46.6055 | 47.1398
medium- and heavy-duty vehicles | 0.044825 | 0.076538 | 0.0902 | 0.1034 | 0.11606 | 0.1284 | 0.13988 | 0.15033 | 0.16053 | 0.17016 | 0.17886 | 0.18688 | 0.19445 | 0.20161 | 0.20866 | 0.21623 | 0.22417 | 0.23318 | 0.24358 | 0.25423 | 0.26469 | 0.27646 | 0.28981 | 0.30384 | 0.31773 | 0.33204 | 0.3472 | 0.36238 | 0.37766 | 0.3946 | 0.41319
buses | 0.35418 | 0.41081 | 0.47197 | 0.52782 | 0.58122 | 0.63279 | 0.68526 | 0.73962 | 0.79476 | 0.85218 | 0.91561 | 0.98605 | 1.0588 | 1.1369 | 1.2217 | 1.3132 | 1.4158 | 1.5282 | 1.6541 | 1.7925 | 1.9507 | 2.1296 | 2.3319 | 2.5665 | 2.8403 | 3.1604 | 3.5493 | 4.0302 | 4.6504 | 5.5182 | 6.8552
Chart: 
| 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
freight rail | 0.4666 | 1.5023 | 3.0189 | 5.0562 | 7.0607 | 11.0675 | 16.7825 | 23.7034 | 31.9704 | 41.4806 | 50.8537 | 60.0701 | 69.0954 | 78.0119 | 85.7634 | 93.7421 | 100.8162 | 108.7814 | 116.3482 | 123.7279 | 130.7157 | 137.6947 | 144.7139 | 151.042 | 156.9866 | 163.0439 | 169.244 | 174.9342 | 180.6895 | 186.5225 | 193.1715
marine | 17.7771 | 40.2856 | 24.8532 | 39.6799 | 45.1281 | 48.492 | 53.4857 | 58.4866 | 59.614 | 59.7752 | 60.5377 | 55.9089 | 57.6021 | 57.6352 | 57.9253 | 58.7257 | 59.403 | 60.5142 | 62.8005 | 62.6452 | 69.2115 | 72.5607 | 75.2818 | 82.4993 | 89.4418 | 91.837 | 96.7375 | 99.0588 | 98.8819 | 99.506 | 98.8324
medium- and heavy-duty vehicles | 43.9587 | 46.9974 | 48.3672 | 48.8409 | 48.7415 | 48.3946 | 47.7695 | 46.9454 | 46.2373 | 45.5873 | 44.9612 | 44.4501 | 44.135 | 44.0935 | 44.283 | 44.7307 | 45.4142 | 46.4348 | 47.7867 | 49.4783 | 51.5859 | 54.128 | 57.0572 | 60.3036 | 63.9594 | 68.0525 | 72.7141 | 77.7491 | 83.1568 | 89.4273 | 96.669
buses | 17.6668 | 20.0355 | 22.0747 | 23.4822 | 24.4926 | 25.1909 | 25.721 | 26.1221 | 26.3588 | 26.4869 | 26.6126 | 26.7485 | 26.7479 | 26.6923 | 26.5978 | 26.4565 | 26.3332 | 26.1805 | 26.0344 | 25.8414 | 25.6791 | 25.5094 | 25.3159 | 25.1417 | 24.9696 | 24.769 | 24.5875 | 24.3873 | 24.1594 | 23.9135 | 23.6751
light-duty vehicles | 1.6616 | 1.6812 | 1.6603 | 1.6438 | 1.5352 | 1.4832 | 1.4375 | 1.3841 | 1.3362 | 1.2901 | 1.2384 | 1.2087 | 1.1809 | 1.1592 | 1.1453 | 1.1345 | 1.1247 | 1.1182 | 1.1163 | 1.0786 | 1.0404 | 1.0462 | 1.0529 | 1.06 | 1.0672 | 1.0771 | 1.0887 | 1.0988 | 1.1116 | 1.1295 | 1.1544
passenger rail | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Delivered compressed and liquefied natural gas by mode
AEO2022 Reference case
quadrillion British thermal units
Delivered electricity by mode
AEO2022 Reference case
quadrillion British thermal units

## Slide 46: Miami Fort Tour 10/6/22
Address: 11021 Brower Road, North Bend, Ohio 45052
  Should be 35-40 minute drive from UC
Please wear closed-toed shoes and long pants
  Hard hats, safety glasses, and ear plugs will be provided, feel free to bring your own if you wish
  There are numerous hazards in the plant, we will discuss safety and any unique risks from operation at the beginning of the tour
  Please bring a photo ID to be used at check-in
  Call my cell if you get lost/have trouble – 937-750-3182

## Slide 47: Site Map/Entry
Brower Rd
Gate 2
“Construction Entrance”
Check in with guard at visitors center first. Then drive over to employee parking lot and meet at south end
Employee Lot
Drive down middle road toward south then turn around to north and park (one-way traffic)