## Slide 1
Four Ways to get Vapor Pressure
Short Cut Method
Approximation
Clausius-Clapyron
Equation
Use Peng-Robinson or other EOS and find where the fugacity ratio is 1
Antoine
Equation
Which method depends on accuracy needed, availability of parameters, and calculation speed required. For Clausius- Clapron Equation you can use 1) ecentricity, 2) critical point, 3) normal boiling point as reference points.
We want to know the vapor pressure to determine fractionation at vapor/liquid equilibria in Chapter 10 for multicomponent systems

## Slide 2
Gibb’s Free Energy decides phase equilibria at constant T and P
-SUV
H A
-pGT
dG=-SdT + VdP (depends on T and P)
GL = GV at equilibrium
dG = VdP (Constant T)

## Slide 3
Vapor/Liquid Equilibria From EOS

## Slide 4
-SUV
H A
-pGT

## Slide 7
At 25°C pure liquid G = 105 kJ/kg – 298°K 0.367 kJ/kg°K = -4 kJ/kg
pure vapor G = 2547 kJ/kg – 298°K 8.56 kJ/kg°K = -4 kJ/kg
-SUV
H A
-pGT
G = H - TS

## Slide 8
-SUV
H A
-pGT
dG = VdP – SdT
At V/L Equilibria
dGL = dGV
VVdPsat – SVdT = VLdPsat – SLdT
(VV-VL) dPsat = (SV-SL) dT
Also
G = H - ST
At equilibrium DGvap = 0
Tvap = DHvap / DSvap
From above
dPsat/dT = DHvap/(T(VV-VL))

## Slide 10
The slope of a plot of lnPsat versus 1/T is -∆Hvap/R (for ideal gas approximation)

## Slide 19
Four Ways to get Vapor Pressure
Short Cut Method
Approximation
Clausius-Clapyron
Equation
Use Peng-Robinson or other EOS and find where the fugacity ratio is 1
Antoine
Equation
Which method depends on accuracy needed, availability of parameters, and calculation speed required. For Clausius- Clapron Equation you can use 1) ecentricity, 2) critical point, 3) normal boiling point as reference points.

## Slide 23
-SUV
H A
-pGT
G = H - ST
Pressure Dependent Formulas

## Slide 25
Arrhenius (1859-1927) Function:
Probability = exp(-DE/kT) or = exp(-DE/RT)
Gives the probability of an event happening if the event is thermally activated; i.e. if the probability changes with the temperature.
Viscosity = Viscosity0 exp(- DEa/kT) Flow happens when atoms thermally move out of the way with an activation energy DEa
Vapor Pressure = P0 exp(-DEvap/kT) Antoine equation
DEvap = DHvap – T DSvap
Psat = P0 exp(A – B/(T+C)) A = – DSvap/R B = DHvap C = Temp for no Psat
Entropy prob. = exp(-S/R) Energy with no enthalpy (Boltzman equation)
Fugacity
f/P = exp((G-Gig)/RT) = probability of a molecule escaping from a phase
G = H - TS is a measure of the balance between enthalpic attractions and thermally driven dispersion of the molecules. So f is a measure of the dispersibility of a phase, the more dispersible the less stable. Lower fugacity is the more stable phase.
Arrhenius accurately predicted global warming due to CO2 in a paper published in 1896 which was widely read. His calculations were within 10% of current global temperature rises.

## Slide 48
P0 = (Pmax+Pmin)/2