## Slide 1: Project 1: Controlling Polymer Rheological Properties Using Long-Chain Branching
PI’s: Ronald Larson1 and Greg Beaucage2
Team: Jimmy Mays3, Nikos Hadjichristidis4, Greg Smith5, Ron Jones6
1 Univ. Michigan; 2 Univ. Cincinnati; 3 Univ. Tennessee; 4 Univ. Athens/KAUST; 5 Oak Ridge National Lab; 6 National Institute of Standards and Technology
Proposed Budget: $150,000/year; In Kind Support ORNL $40,000/year; NIST $40,000/year
Project Duration: 4 years
Notes: <number>

## Slide 2: Outcomes/Deliverables
Inference of long-chain branching structures from rheological, neutron scattering, SEC, and other measurements.
Development of computer software for inference of long-chain branching structure from characterization data and catalyst information
Inference of nonlinear rheology and processing characteristics from branching structure
Tools for optimization of branching
Innovation through Partnerships
<number>

## Slide 3: Impact
Improved ability to design and control polymer processing properties
Ability to infer likely branching characteristics from rheology
Understanding of complex catalyst systems and resolution of some longstanding debates over molecular structure in certain resin systems
Innovation through Partnerships
<number>

## Slide 4: Supplementary Material
Innovation through Partnerships
<number>

## Slide 5: Industrial Relevance
“The flow behavior (‘rheology’) [of polymers] is enormously sensitive to LCB [long chain branching] concentrations far too low to be detectable by spectroscopic (NMR, IR) or chromatographic (SEC) techniques. Thus polyethylene manufacturers are often faced with ‘processability’ issues that depend directly upon polymer properties that are not explainable with spectroscopic or chromatographic characterization data. Rheological characterization becomes the method of last resort, but when the rheological data are in hand, we often still wonder what molecular structures gave rise to those results.”
        Janzen and Colby, J. Molecular Structure, 1999
Innovation through Partnerships
<number>

## Slide 6: Rheology, Processing and Long-Chain Branching
Innovation through Partnerships
<number>
< 1 LCB’s per million carbons significantly affects rheology!
branched thread-like micelles
branched polymers

## Slide 7: Blends of Linear Exact 3128 and Branched PL1880 Polyolefins
<number>
X.Chen, C. Costeux, R. Larson. J. of Rheology 54(6) 1185-1206, 2010
Notes: <number>

## Slide 8: Rheology of Blends of Linear Exact 3128 and Branched PL1880 Polyolefins
<number>
T=150C
Increasing LCB
<1 LCB per million carbons!
Notes: <number>

## Slide 9: A Priori Predictions of Commercial Branched Polymer Rheology with Levels of LCB down to one Branch per Million Backbone Carbons
<number>

## Slide 10: Small-Angle Neutron Scattering
<number>
Branch content of metallocene polyethylene Ramachandran R, Beaucage G, Kulkarni AS, McFaddin D, Merrick-Mack J, Galiatsatos V Macromolecules, 42 4746-4750 (2009).

## Slide 11: Metallocene Resins
<number>
Branch content of metallocene polyethylene Ramachandran R, Beaucage G, Kulkarni AS, McFaddin D, Merrick-Mack J, Galiatsatos V Macromolecules, 42 4746-4750 (2009).

## Slide 12
<number>

## Slide 13: Branches per Chain Compare Catalysts
<number>

## Slide 14: Hyperbranch Content Compare Catalysts
<number>

## Slide 15: Proposed Work
<number>
-Scaling Method: Beaucage has developed a new method for the quantification of macromolecular topology, that can be used to analyze small-angle scattering data. The method yields unique parameterization of the average branch length, number of inner segments (branch on branch or hyperbranch content) and quantitative (with error bars) measures of the number of branches, mole fraction branches as well as a number of other parameters.
-Linear Rheology: We propose to combine this new method with methods developed in the Larson group for inferring branching structures from linear rheology data and catalyst reaction pathways to improve determination of branching structures in polymers of industrial importance.
-Non-Linear Rheology: This will be combined with predictions of nonlinear rheology to determine how to tailor branching levels to obtain optimal processing behavior.