## Slide 1: Project 2: Adsorption, Adhesion, and Topology of Linear and Branched Macromolecules on Curved and Flat Surfaces
PI’s: Peter Green1, Vikarm Kuppa2, Steve Clarson2, Rick Laine1
Team: Jimmy Mays3, Nikos Hadjichristidis4, Greg Smith5
1 Univ. Michigan; 2 Univ. Cincinnati; 3 Univ. Tennessee; 4 Univ. Athens/KAUST; 5 Oak Ridge National Lab
Proposed Budget: $150,000/year; In Kind Support ORNL $40,000/year
Project Duration: 3 years
Notes: <number>

## Slide 2: Outcomes/Deliverables
Insight into polymer absorption, adhesion, surface layer structure, dynamics of absorption as a function of chain topology.
Synthesis of topologically relevant model siloxanes.
Interfacial effects as a function of topological evolution.
Optimization of chain topology for controlled interfacial properties.
Innovation through Partnerships
<number>

## Slide 3: Impact
New information and insight into adhesion an absorption.
Understand synthesis/structure/property relationships for new products.
Understanding of complex systems involving polymer/inorganic interfaces with polymer chains of complex topology.
Innovation through Partnerships
<number>

## Slide 4: Supplementary Material
Innovation through Partnerships
<number>

## Slide 5: Industrial Relevance
Innovation through Partnerships
<number>
The nature of polymer/surface interactions for supported polymer films, of polymer composites used in different applications is often not well understood.
The role of chain branching is even less understood. Recent evidence strongly suggests that effects associated with branching are far more significant than one would have previously imagined.
With the suite of techniques and theory we could develop an understanding that enable the development of predictive models.
The understanding we develop would have a long-term impact on materials design and processing for different applications

## Slide 6: Adsorption of polymers at interfaces
Innovation through Partnerships
<number>
Innovation through Partnerships
<number>
substrate
Adsorbed layers
Nanocomposite
Thin Film
CHALLENGE: The nature of the interactions between macromolecules and interfaces (adhesion, adsorption) play an important role in the performance of thin films and polymer composites. Thin polymer films are used in a range of applications that include: adhesives, active and passive coatings and sensors. Polymer composites, which include macroscopic fillers and nano-fillers, have diverse applications, from tires to solar cells.

## Slide 7
<number>
Goals
GOAL: We propose to understand interactions at interfaces between polymers and surfaces in two types of systems: (1) thin polymer films on surfaces; (2) fillers (e.g.: silica) in polymer hosts. The fillers will range in size from the nano-scale to microns.
EXPERIMENTS: (1) Dielectric spectroscopy to examine the adsorption of chains from a melt to flat and curved surfaces. (2) Spectroscopic ellipsometry, to examine adsorption to flat interfaces; (3) Use of AFM to study adhesion and friction at interfaces; (4) Neutron and x-ray reflectivity to study surface composition profiles.
Notes: <number>

## Slide 8: OUTCOME AND DELIVERABLES
  We can work with systems provided by industry.
  Study a polymer (polyolefin) with silica particles of different sizes
    Polymer/SiOx substrates to study surface time-dependent adsorption using dielectric spectroscopy
    Use spectroscopic ellipsometry to study Tg changes
    Measurements could be done using linear and branched macromolecules
    AFM measurements of adhesion, deformation, friction
  We could prepare polymer nanocomposites of identical materials (polymer, silica, linear, branched) to the above and study Tg and dynamics
  With the suite of techniques and theory we could develop an understanding that enable the development of predictive models.
Innovation through Partnerships
<number>

## Slide 9
Tuning adsorbed structure (MC Simulations)
Topology of the adsorbed layers can be controlled
Loops
Tails
Trains
Distributions are dependent on PDI and ε

## Slide 10
<number>
Adsorbed structure (MC Simulations)
PDI = 1.01 PDI = 1.78
Notes: <number>

## Slide 11
Tuning adsorbed structure
Control adsorbed layer topology
dispersion (ex: nanoparticles)
Entanglements through loops
reinforcement
Surfactant efficacy and wettability
Surface coverage and protection
Fundamental insights into equilibrium and metastable structures, thermodynamics and kinetics

## Slide 12: The strong adsorption of chains onto fillers in a composite
Innovation through Partnerships
<number>
Dielectric spectroscopy could be used to examine the
Host chain dynamics
The dynamics of chains that are adsorbed strongly t a substrate
Differences between the adsorption of linear and branched chains in composite

## Slide 13
Cantilever Deflection
A
B
C
E
D
F
Retraction
Piezo displacement
Retraction
A
F
B
C
D
E
Approach
Approach
Force Measurements with AFM
Force Measurements with AFM using a silica particle to measure: adhesion, friction, deformation
The AFM measurements can be performed by placing a silica particle at the end of the tip and measuring the adhesion, stiffness and deformation of linear and branched chains
Notes: <number>

## Slide 14: AFM Measurement of Stiffness, Deformation and Adhesion
We propose to examine the mechanical properties of the surface of our samples using AFM based on an analysis of the measured the force-distance (FD) curves of a series of samples.
The forces on the tip can be accurately controlled from 10 nN to over 4000 nN across an arrayA typical force distance curve is shown. The effective stiffness, S, and adhesion are determined as shown in the Figure.
Innovation through Partnerships
<number>
A schematic of load-vs-depth (deformation of material during loading). The effective stiffness, S, of the material can be calculated from the linear part of the unloading curve.

## Slide 15
Linear and branched chains of the same chemistry may exhibit different surface wetting characteristics
AFM images of linear and star shaped polystyrene on silicon oxide substrates. The contact angle of the linear chain is ~22 degrees, whereas that of the 8-arm star is ~3 degrees.
The interactions between linear chains and a substrate are different from that of and branched molecule, of the same chemistry, with the same substrate.
This is primarily because the branched molecules suffer a smaller entropic energy losses on adsorption to the surface.
Glynos, Frieberg, Green, Physical Review Letters, 2011

## Slide 16: OBJECTIVES
Three systems are proposed:
  Polyolefin/SiOx substrate thin film
    The commercial polymers could be branched and unbranched
  Polymer silica nanocomoposite
    the silica particles vary in size from nanometers to microns)
OBJECTIVES
  Understand adsorption of linear and branched molecules unto flat surfaces
  Understand the adhesion and friction of the free surface of branched and linear chain polymers
  Study the dynamics and glass transition of linear and branched chains onto silica particles in polymer nanocomposites
Innovation through Partnerships
<number>