## Slide 1: Project 3: Effect of Branching on Flow-Induced Crystallization and Crystalline Orientation of Polyolefins
PI’s: Mike Solomon1, Greg Beaucage2, Ryan Breese3, Ron Larson1
Team: Jan Ilavsky4, Jimmy Mays5, Nikos Hadjichristidis6
1 Univ. Michigan; 2 Univ. Cincinnati; 3 Eclipse Film Technologies; 4 Argonne National Lab; 5 Univ. Tennessee/ORNL; 6 Univ. Athens/KAUST
Proposed Budget: $150,000/year; In Kind Support Eclipse Film Technologies $75,000/year, Argonne National Lab $25,000/year, ORNL $25,000/year
Project Duration: 4 years
Notes: <number>

## Slide 2: Outcomes/Deliverables
Innovation through Partnerships
<number>
Correlation of polyolefin branching structure on crystallization kinetics, crystallization morphology (e.g. spherulite size and density) and orientation.
Quantification of effect of linear and long- and short-chain branched fraction on polyolefin crystallization kinetics and morphology
Measurements of interaction of branching structure and shear deformation on crystallization kinetics, orientation and morphology
Development of scattering and rheological tools to probe effect of branching on crystallization

## Slide 3: Impact
Innovation through Partnerships
<number>
Improved ability to link long chain branching structure to crystallization kinetics, crystallization morphology and orientation of polyolefins
Potential to manipulate crystallite morphology (e.g. size, density and orientation) by means of polyolefin branching structure
Processing/structure interaction in long and short chain-branched polyolefins.

## Slide 4: Prior work and project scope
A comb-shaped long-chain branched molecule added at approximately the overlap concentration significantly increased the crystallization kinetics of a hydrogenated polybutadiene blend1
Isotactic polypropylenes of varying branching index showed enhanced crystallization kinetics and oriented crystallites due to long chain branching2
Innovation through Partnerships
<number>
1E.L. Heeley et al., “Shear-induced crystallization in blends of model linear and long-chain branched hydrogenated polybutadienes,” Macromolecules, 39, 5058 (2006).)
2P.K. Agarwal et al, “Shear-induced crystallization in novel long chain branched polypropylenes by in situ rheo-SAXS and -WAXD,” Macromolecules, 36, 5226 (2003);
To extend the state-of-the-art, we should apply an integrated set of scattering, rheology and modeling studies to a series of polyolefin materials in which long-chain branch structure is homologously varied.

## Slide 5: Prior work and project scope
Beaucage in collaborative work with LyondellBasell over a number of years has published in this area , J. of Polym. Sci. B 39, 2923-36 (2001); 45, 1834-44 (2007); 46, 607-18 (2008); Polymer 42, 3103-13 (2001); 44, 1103-15 (2003); Curr. Opin. In Sol. St. Mat. Sci. 8 436-48 (2004).
These papers detail the use of SAXS and WAXS to understand the relationship between the properties of polyolefin films and the nano- and crystallographic structure and orientation.
Orientation in processed films is linked to long chain branching.
Innovation through Partnerships
<number>

## Slide 6: Supplementary Material
Innovation through Partnerships
<number>
Bafna/Beaucage et al. Polymer 44, 1103-15 (2003)

## Slide 7
Innovation through Partnerships
<number>
Breese/Beaucage et al. J. of Polym. Sci. B 46, 607-18 (2008)

## Slide 8: Shear-induced crystallization of polypropylene
(Kumaraswamy et al., 1999)
Spatially dependent PP crystallization
in cross slot flow
(gap = 0.5 mm, w =0.05 MPa, ts = 4 s)
cross slot flow profile
Polarized light micrograph
spherulitic core
oriented skin
• crystallization kinetics and morphology affected by shear
• controlled experiments with short shear times best model processing conditions
(Liedauer et al., 1993)
• crystallization time depends on Mw,  and ts
•

## Slide 9: Methods: light scattering
Freq. Doubled Nd-Yag
= 532 nm
waveplate
focusing lens
polarizer
collimating lens
mirror
polarizer
pin hole
detection lens
12-bit
CCD camera
beam stop
pin hole
Linkam shearing hotstage
1 s-1 < γ’ < 60 s-1
50 μm gap
a = 4.000.29 m

## Slide 10: Master curve behavior: effect of shear strain
For PP nanocomposites, effect appears to scale with strain over range probed

## Slide 11: Project will present a comprehensive understanding of topological control over crystallinity in processing
-Growth rate and structural effects under controlled shear
-In situ and ex situ orientation studies of crystallographic and nano-structures
-Study of cold drawing through MDO processing of films produced from branched polyolefins
-Use of model polymers and commercial grade polymers